## Slide 1
Dave Biersach
dbiersach@bnl.gov
Board 01
CircuitPython, GPIO, NeoPixels, RC Circuit
Control System Electronics 101
Using Python and Sensors to Measure Circuits

## Slide 2: Welcome!
My name is Dave Biersach
I am a Senior Technology Architect at BNL
I am a 1989 graduate of the United States Military Academy at West Point, and I served in the Persian Gulf War as a Combat Engineer
I developed satellite counter-reconnaissance search algorithms while working for DARPA
I have worked at Microsoft & Pfizer
I have been married for 35 years, have three adult children, two dogs, and have sponsored interns for the past 17 years

## Slide 3: The US Department of Energy
17 National Labs across the USA
National Nuclear
Safety Administration
Student research opportunities exist at all US Labs

## Slide 4
https://www.bnl.gov

## Slide 5: About Brookhaven National Laboratory
YouTube - This is Brookhaven Lab

## Slide 6: What is Scientific Computing?

## Slide 7: What is Scientific Computing?
Scientific computing problems cannot be solved using just a graphing calculator or a spreadsheet program
  A computer should not be viewed as just another closed-form benchtop instrument with fixed functionality
  SciComp does not require writing thousands of lines of code to answer problems – complete code usually fits on one slide!
SciComp is applied computer science
  The first name of CompSci is computer
  The first name of SciComp is science
  A triple helix of math, science, and computing

## Slide 8: SciComp vs CompSci
Probability and Statistics
Simulation and Modelling
Data Visualization
Storing and Analyzing Very Large Datasets
Parallel & Distributed Algorithms
Speed and Accuracy Paramount
Functional Languages
Open-Ended Problems with Unknown Solutions
General Data Structures
Design Methodologies
Procedural Languages
Stand-Alone Programs
Emphasis on Object-Orientation
Simple Data Models
Sequential Algorithms
Less Graphics Intensive
Directed Closed-Form Problems with Known Solutions
Scientific Computing
Computer Science

## Slide 9: SciComp = Just Enough CompSci
Data types: int, float, bool, string
Data structures: lists, arrays, dictionaries, classes, modules
Functions: def, return
Statements: if, for, while, break
Patterns: vectorization, divide & conquer, map-reduce
Algorithms: GCD, mean/variance, sorting, searching
Modules: numpy, matplotlib, numba, scipy, sympy, scikit-learn

## Slide 10: Scientific Computing with Python
Python is quickly becoming one of the most heavily used languages in science projects
Python runs on all major modern operating systems and is completely free and open-source (not vendor-controlled)
Python makes it easy for your code to directly integrate with a large spectrum of available 3rd party software
Python code runs consistently on different platforms and scales well from small IoT devices to large server clusters
Python benefits from a very active and growing user community that continues to enhance the language
200,000+ free/open-source packages are readily available!

## Slide 11: Example SciComp Topic Multidimensional Interpolation
YouTube - Jonsey Reports

## Slide 12: Example SciComp Topic Multidimensional Interpolation
Modi (Brave) and Magni (Strong)

## Slide 13: Example SciComp Topic Multidimensional Interpolation
A first order 3-D approximation of the ocean floor based upon only 220 sample (red) points (sonar timings)

## Slide 14: SciComp As Translational Science
SciComp is the ability to translate mathematical expressions of scientific concepts into correct and efficient software code
"The algorithm that almost won the cold war"
11 lines of code can change the world!

## Slide 15
https://www.bnl.gov/newsroom/news.php?a=26599

## Slide 16
https://www.bnl.gov/newsroom/news.php?a=213064

## Slide 17: SciComp = The Pathway to Internships

## Slide 18
SciComp = The Pathway to Internships
High school interns at CERN are required to complete a course in Scientific Computing before they can begin their internship.
That is how important CERN views these skills!

## Slide 19
BNL Science Undergraduate Laboratory Internship (SULI)
https://www.bnl.gov/education/programs/program.php?q=188

## Slide 20: About BNL's College Internships
YouTube - Summer Internship Programs at Brookhaven Lab

## Slide 21: Control Systems Engineering
Modern science is critically dependent on the precision and reliability of control systems built and maintained by engineers and technicians
This hands-on workshop will teach the fundamentals of programming microcontrollers to automate the acquisition and analysis of experimental data measured from analog and semiconductor circuits
You will write Python code to control high-precision sensors that can rapidly measure and plot the transient reactions of various electronic components
These skills are precisely what the US Department of Energy is looking for across all 17 National Laboratories!

## Slide 22: 2026 Mini-Semester (Tech/Engr Track)

## Slide 23: Download the CSE101 Courseware
The CSE101 courseware is in a GitHub repository here:
https://github.com/dbiersach/cse101
The bottom of that page has a link to the slides:



## Slide 24: Download the CSE101 Courseware
The CSE101 course uses three open-source (and free $$$) tools: git, uv, and VS Code
  The next few slides show how to install these tools using WinGet (for Windows) or Homebrew (for macOS)
  If you cannot use WinGet or Homebrew on your PC, manual installation instructions are on the slides at the end
If you have these three tools already installed on your PC, you do not need to reinstall them
  Ensure all three are updated to the latest version
  Be sure you can launch git, uv, and code from a terminal session on your PC

## Slide 25: (Windows) Step 0 – Update winget
winget list --id Microsoft.AppInstaller
winget upgrade Microsoft.AppInstaller


https://learn.microsoft.com/en-us/windows/package-manager/winget
Start a Windows Terminal session, then enter these commands:

## Slide 26: (Windows) Step 1 – Install Tools
winget install Microsoft.VisualStudioCode
winget install Git.Git
winget install astral-sh.uv

## Slide 27: (Windows) Step 2 – Install Courseware
Start a new Windows Terminal session, then enter these five commands:
git clone https://github.com/dbiersach/cse101
cd cse101
.\install_vscode_extensions.ps1
uv sync
code .\cse101.code-workspace

## Slide 28: (Windows) Step 2 – continued

## Slide 29: (Windows) Step 2 – continued

## Slide 30: (Windows) Step 3 – Trust the Workspace

## Slide 31: (Windows) Step 4 – Open welcome.py

## Slide 32: (Windows) Step 5 – Select Interpreter

## Slide 33: (Windows) Step 6 – Run welcome.py

## Slide 34: (Windows) Step 6 – continued

## Slide 35: (macOS) Step 0 – Install Homebrew
https://github.com/Homebrew/brew/releases/download/5.0.8/Homebrew-5.0.8.pkg
Only do this if you do not already have Homebrew installed on your Mac…

## Slide 36: (macOS) Step 1 – Install Git
brew install git
In a new Terminal window…

## Slide 37: (macOS) Step 2 – Install VS Code
brew install --cask visual-studio-code
In the same Terminal window…

## Slide 38: (macOS) Step 3 – Install Astral “uv”
https://docs.astral.sh/uv/getting-started
In the same Terminal window…
brew install uv

## Slide 39: (macOS) Step 4 – Clone SciComp101 Repo
git clone https://github.com/dbiersach/scicomp101
In a new Terminal window…

## Slide 40: (macOS) Step 5 – Install VS Code Extensions
cd scicomp101
bash ./install_vscode_extensions.sh
In the same Terminal window…

## Slide 41: (macOS) Step 6 – Create Python .venv
uv sync
In the same Terminal window…

## Slide 42: (macOS) Step 7 – Open the Workspace

## Slide 43: (macOS) Step 8 – Trust the Workspace

## Slide 44: (macOS) Step 9 – Open welcome.py

## Slide 45: (macOS) Step 10 – Select Interpreter

## Slide 46: (macOS) Step 11 – Run welcome.py

## Slide 47: (macOS) Step 11 – continued

## Slide 48: Open This Slide Deck
This is the Board 01 PowerPoint Deck
We are currently viewing slide #48

## Slide 49: Board 01 – Goals
Compare and contrast a microcontroller unit (MCU) with a central processing unit (CPU)
Gain familiarity with the Raspberry Pi Pico board that uses an RP2040 MCU
Understand the value of Adafruit’s CircuitPython and its Blinka layer that runs on personal computers and SBCs
Review Adafruit’s u2if firmware that connects your PC to the RP2040 ports and protocols

## Slide 50: Unpacking Your Student Kit A
Each student has a numbered “A” kit – record your kit ##
Gently open your kit then take a picture of it before unpacking it – please repackage it the same way
(4) Breadboards {Numbered 01, 02, 03, 04}
(1) Raspberry Pi Pico microcontroller
(1) Silver braided USB-A (Male) to USB-B Micro (Male) cable
(1) USB-A (Female) to USB-C (Male) adapter
(3) Black and (3) Red jumper cables (Male to Male)
(2) Yellow and (2) Blue jumper cables (Male to Male)
(1) 200 mm Qwiic / STEMMA QT cable (JST SH 4-Pin)

## Slide 51: Unpacking Your Student Kit (A)
(3) Red
(3) Black
(2) Blue
(2) Yellow
(1) Qwiic / STEMMA-QT

## Slide 52: What is a Microcontroller Unit (MCU)?
https://en.wikipedia.org/wiki/Microcontroller

## Slide 53: CPU vs MCU
Runs many programs simultaneously
Large size (billions of transistors)
32+ execution Cores
Extremely high speed (+4GHz)
High Power Consumption
Large Addressable Memory (TB)
Advanced Mathematics Functions
Designed to run Operating Systems
Low Volume / High Cost
Central Processing Unit (CPU)
Often runs only a single program
Small size (thousands of transistors)
2 execution Cores
Generally Slower (133MHz)
Very Low Power Consumption
Smaller Addressable Memory (KB)
Simple Mathematics Functions
Often runs NO operating system
High Volume / Low Cost
Microcontroller Unit (MCU)
Intel Core Ultra 9 = $589
Raspberry RP2040 = $0.80

## Slide 54: What is a Microcontroller Unit (MCU)?

## Slide 55: What is a Microcontroller Unit (MCU)?
https://www.raspberrypi.com/documentation/microcontrollers/silicon.html
Raspberry Pi Foundation
RP2040 MCU

## Slide 56
$5.00
https://www.adafruit.com/product/5525

## Slide 57: What is Adafruit?
Earned her Masters Degree in Electrical Engineering from MIT
$150M revenue in 2025

## Slide 58
https://www.adafruit.com/product/5905
$4.50

## Slide 59: Adafruit CircuitPython
https://circuitpython.org

## Slide 60: Adafruit Blinka
https://circuitpython.org/blinka

## Slide 61: Adafruit Blinka
https://circuitpython.org/blinka/raspberry_pi_pico

## Slide 62: Adafruit Blinka
Adafruit Blinka allows you to run CircuitPython code directly on your PC
This contrasts with the standard Circuit Python setup:
  Normally, the CircuitPython runtime is first installed on a microcontroller
  Then you download and run a CircuitPython script directly on the microcontroller
  With Blinka, you don’t have to download a Python script to the microcontroller – only your PC runs Python code
The Adafruit u2if firmware via the Blinka layer makes your PC “believe” it has GPIO pins, buses (such as Serial, SPI, I2C) and two ADC ports

## Slide 63: Adafruit u2if Firmware
https://learn.adafruit.com/circuitpython-libraries-on-micropython-using-the-raspberry-pi-pico/running-circuitpython-code-without-circuitpython
u2if = USB to interfaces

## Slide 64: Adafruit u2if Firmware Pinout
NOTE: I have already preloaded the latest version of the u2if firmware onto your Pi Pico

## Slide 65: Wiring Each Board
The Pi Pico connects to your PC using the silver cord
  The USB-A (Male) connector is inserted into your PC
  The USB-B Micro (Male) is inserted into the Pi Pico
Please do not remove the Pi Pico from the Under Plate
If you incorrectly wire your lab, you can permanently damage your laptop’s USB port—double-check everything!
Connect the Pi Pico after you have connected all required silicon jumper wires (and the Qwiic cable if needed for the lab) to the components on the breadboard
NOTE: I have already preloaded the latest version of the u2if firmware onto your Pi Pico boards

## Slide 66: Example Lab Wiring

## Slide 67: Jumper Wires
https://www.adafruit.com/product/4482

## Slide 68: Jumper Wires
https://www.amazon.com/gp/product/B0002H7AIG

## Slide 69
$1.25
https://www.adafruit.com/product/4401
STEMMA QT / Qwiic Cable – 200mm

## Slide 70: Board 01 – Goals (cont.)
Develop intuition about the relationships between voltage, current, resistance, and power
Map the power rails and tie point rows on a breadboard to the underlying wiring connectivity
Learn what a Digital Multimeter (DMM) is and how it compares to the capabilities of a Multi-function Tester
Review standard analog discrete components, including a resistor, a capacitor, and a light-emitting diode
Run CircuitPython code via Blinka to drive an LED using pulse width modulation (PWM)

## Slide 71: What is a Current?
Conventional Current Flows from + to -
Actual Current Flows from - to +
Current = Moving Electrons

## Slide 72: Voltage, Current, Resistance
V = Voltage
Volts (V)
I = Current
Amps (A)
R = Resistance
Ohms ()
Alessandro Volta
(1745 – 1827)
André Ampère
(1775 – 1836)
Georg Ohm
(1789 – 1854)
Potential Energy
Amount
of Flow

## Slide 73: Voltage, Current, Resistance

## Slide 74: Voltage, Current, Resistance
James Watt
(1736 – 1819)
Ohm's Law
Current
Volts
Resistance
A Circuit
Schematic
Joules (Energy) per second

## Slide 75: Voltage, Current, Resistance
All metal wires have some
(a very tiny amount) of
natural internal resistance!
If resistance is low,
and voltage is high,
a current can generate
a lot of HEAT (Watts)

## Slide 76: Voltage, Current, Resistance
Pay strict attention to wiring pictures and schematics
Do not cross +V and GND wires
All team members must doublecheck each other's circuits prior to turning on the power
Unplug any circuit that is getting hot – do not touch the board!
Completely unplug every circuit prior to changing any wiring
Immediately report any problems
SAFETY First!

## Slide 77: Breadboard Wiring
+V
GND
In direct current (DC) circuits, positive voltage (+V, VCC , VDD) is usually colored RED
In direct current (DC) circuits, the “zero reference” voltage (GND, COM, VSS) is usually colored BLACK or BLUE
It is common in direct current circuits to connect a negative terminal to Ground (GND)
The holes along each outside vertical column are electrically connected and are called a power rail or a power bus

## Slide 78: Breadboard Wiring
+V
GND
In direct current (DC) circuits, positive voltage (+V, VCC , VDD) is usually colored RED
In direct current (DC) circuits, the “zero reference” voltage (GND, COM, VSS) is usually colored BLACK or BLUE
The holes along each outside vertical column are electrically connected and are called a power rail or a power bus

## Slide 79: Breadboard Wiring
Rows of five holes (tie-points) on either side of the middle
(DIP Support) channel are electrically connected
These two wirings accomplish the same thing
All three of these wires are electrically connected

## Slide 80: Breadboard Wiring

## Slide 81: Test Your Understanding
What is the voltage at the free end of each of these wires?
+5V
GND
GND
+3.3V





GND
+5V
GND
+3.3V
Meltdown
A short circuit!

## Slide 82: Review Board 01
Board 01 will introduce you to simple GPIO coding by flashing an external LED, driving a NeoPixel, reading the status of a push button, and measuring a series RC circuit
LED
NeoPixel
Push Button




RC Circuit

## Slide 83: What is a Resistor?
A resistor is a passive two-terminal electrical component that implements electrical resistance as a circuit element. In electronic circuits, resistors are used to reduce current flow, adjust signal levels, to divide voltages, and bias active elements
The electrical function of a resistor is specified by its resistance: common commercial resistors are manufactured over a range of more than nine orders of magnitude. The nominal value of the resistance falls within the manufacturing tolerance, indicated on the component
½ Watt Resistors
1% Tolerance

## Slide 84: What is a Digital Multimeter (DMM)?
A DMM is a standard test and measurement instrument used by engineers and technicians to measure multiple electrical stimuli, including voltage, current and resistance
It combines the features of a voltmeter, ammeter and ohmmeter, and is used to verify the state of a system or circuit for safety purposes
= Measure voltage (volts)
= Measure resistance (ohms)
= Measure capacitance (farads)
V
Ω
-||-
Turn the dial to select the measurement you want to take for the component attached to the DMM leads
BLACK
RED

## Slide 85: Measuring a Resistor with a DMM
Turn the dial to Ω to measure in ohms the resistor

## Slide 86: Measuring a Resistor with a DMM
The units might be difficult to see – here the measurement is 10.02 kiloohms
= "kilo-"
is one thousand
= "mega-"
is one million

## Slide 87: Purchase a Digital Multimeter (DMM)
https://www.sparkfun.com/products/18340

## Slide 88: What is a Diode?
A diode is a semiconductor device that essentially acts as a one-way switch for current. It allows current to flow easily in one direction, but severely restricts current from flowing in the opposite direction
The forward voltage (Vf) is the amount of voltage needed to get current to flow across a diode. This is important to know because if you are trying to push a signal through a diode that is less than the forward voltage, you will be disappointed
1N4001 Diode
Anode
+
Cathode
-

## Slide 89: Measuring a Diode with T7 Tester
Press the Start button to begin measuring the DIODE values
The Vf value is displayed on the screen

## Slide 90: Purchase a T7 Tester
https://www.amazon.com/gp/product/B09KGXTVBR

## Slide 91: What is a Light Emitting Diode
In a diode, there is a PN junction, where P-type semiconductor material (with electron “holes”) touches N-type semiconductor material (with excess electrons)
When current is applied in the forward direction, electrons from the N-type material are pushed toward the junction. Simultaneously, “holes” from the P-type material move toward the junction from the opposite direction
At the junction, electrons from the conduction band (higher energy) recombine with holes in the valence band (lower energy). This recombination releases energy as photons (light) rather than heat, making the process highly efficient

## Slide 92: What is a Light Emitting Diode?

## Slide 93: Wire Your Pico to Board 01
Don’t move short jumper wires
NEVER remove components from any breadboard
Black to GND
Yellow to (GP)IO22 pin

## Slide 94: Wire Your Pico to Board 01
Black to GND
Yellow to (GP)IO22 pin
A circuit must have a closed loop for electrons to flow, enabling a current

## Slide 95: Wire Your Pico to Board 01
A 330Ω Resistor limits the current flowing through the LED so it doesn’t burn out
Black to GND
Yellow to (GP)IO22 pin

## Slide 96: Wire Your Pico to Board 01
Point the silver part of the jumper wire pin towards you

## Slide 97: Open blink_led.py







## Slide 98: Connect the Pico to your PC
Plug the USB connector into your PC

## Slide 99: Run blink_led.py
What is happening to the LED and why?

## Slide 100: Dimming an LED via PWM
To dim an LED, we need to provide a variable voltage to the diode between 0V and 3.3V
An RP2040 microcontroller can output only a fixed 3.3V
However, we can simulate a variable output voltage by using pulse width modulation (PWM)
PWM turns a GPIO output pin quickly on and off, and the resulting average voltage (over some unit of time) is what appears to drive the attached component
The ratio of time the GPIO pin is High vs. Low (the duty cycle) determines the perceived fractional output voltage

## Slide 101: Dimming an LED via PWM

## Slide 102: Open pwm_led.py







In Hz, for a full cycle
/ 65535 yields (0 – 100)%

## Slide 103: Run pwm_led.py
What is happening to the LED and why?

## Slide 104: Board 01 – Goals (cont.)
Control an Adafruit NeoPixel to emit different colors
Use a debounce library to simplify avoiding the electrical noise (jitter) coming from a low-cost push button
Compare and contrast an Analog to Digital Converter (ADC) versus a Digital to Analog Converter (DAC)
Understand Kirchhoff's two Circuit Laws (KCL + KVL)
Derive and solve a differential equation expressing the voltage over time of an RC circuit as it charges
Graph the circuit response of a resistor and a capacitor connected in series to compare the theoretical vs. actual voltage over time

## Slide 105: Adafruit made NeoPixels fun!
In 2007, the WorldSemi company created the WS2812-compatible family of addressable color LEDs
In 2013, Limor Fried (founder of Adafruit, also goes by Ladyada) branded these RGB LEDs as NeoPixels and provided extensive documentation, libraries, and support for these LEDs, making them a staple in the maker and DIY electronics community
https://www.adafruit.com/category/168

## Slide 106: Unplug the MCU before changing any wiring!
As we move between each “experiment” on a given breadboard, or when we switch to an entirely new Board #, it is crucial that your FIRST UNPLUG the USB cord!
I recommend unplugging the cord at the PC end – leave the cord connected to the Micro USB port on the Pico
It is dangerous to change any wiring while the MCU is still drawing power from your laptop’s USB port
If you incorrectly connect a jumper wire between the Pico and the breadboard while the Pico is drawing power from your PC, you can permanently damage your PC’s USB port
Have your partner double-check your wiring every step!

## Slide 107: Wire Your Pico to Board 01
Black to GND
Red to 3.3V
Yellow to (GP)IO22 pin

## Slide 108: Wire Your Pico to Board 01
Only one control wire is required!
Black to GND
Red to 3.3V
Yellow to (GP)IO22 pin

## Slide 109: Open cycle_neopixel.py











## Slide 110: Connect the Pico to Your PC
Plug the USB connector into your PC

## Slide 111: Run cycle_neopixel.py
Check out the NeoPixel on your Board 01

## Slide 112: Unplug the MCU before changing any wiring!
As we move between each “experiment” on a given breadboard, or when we switch to an entirely new Board #, it is crucial that your FIRST UNPLUG the USB cord!
I recommend unplugging the cord at the PC end – leave the cord connected to the Micro USB port on the Pico
It is dangerous to change any wiring while the MCU is still drawing power from your laptop’s USB port
If you incorrectly connect a jumper wire between the Pico and the breadboard while the Pico is drawing power from your PC, you can permanently damage your PC’s USB port
Have your partner double-check your wiring every step!

## Slide 113: Wire Your Pico to Board 01
Blue to
(GP)IO20 pin
The code will set
GPIO Pin #20
to be in a PULL-UP mode
This button is NORMALLY OPEN
Black to GND
Red to 3.3V

## Slide 114: General Purpose I/O Pins (GPIO)
+3.3V
An internal pull-up resistor inside the RP2040 will keep the GPIO input from floating while the button is normally open
When the button is pressed, the path of least resistance connects the GPIO to GND
We can consider this configuration to be ACTIVE LOW
This means when the GPIO pin goes LOW
(to GND or 0 Volts)
it indicates the user pressed the button

## Slide 115: The Real World is Noisy
https://learn.adafruit.com/debouncer-library-python-circuitpython-buttons-sensors

## Slide 116: Open button_debounce.py







## Slide 117: View button_debounce.py








## Slide 118: Connect the Pico to Your PC
Plug the USB connector into your PC

## Slide 119: Run button_debounce.py
Press the push button repeatedly – what does the NeoPixel do?

## Slide 120: Review Board 01
We will now analyze the final circuit on Board 01, which is a series Resistor-Capacitor (RC) circuit

## Slide 121: What is a Capacitor?
A capacitor is a device that stores electrical energy in an electric field by virtue of accumulating electric charges on two close surfaces insulated from each other
The main function of capacitors is to store electrostatic energy in an electric field, and give this energy to the circuit, when necessary

## Slide 122: Ceramic vs. Electrolytic Capacitors
The longer lead is usually the anode (+)
The shorter lead is usually the cathode (-)

## Slide 123: Measuring Electrolytic Capacitor with a DMM
Turn the dial to -||- to measure in farads the electrolytic capacitor

## Slide 124: Measuring Electrolytic Capacitor with a DMM
The units might be difficult to see – here the measurement is 10.98 microfarads

## Slide 125: ADC (input) vs. DAC (output)
ADC = Analog to Digital Converter
Reads a voltage between +3.3V to GND and returns an integer between 0-65,535:
65,535 = +3.3V, 0 = GND
DAC = Digital to Analog Converter
Given an integer between 0 and 65,535 the MCU outputs a fixed voltage:
65,535 = +3.3V, 0 = GND
RP2040 can sense only 4,096 distinct voltage levels
The RP2040 does NOT have a true DAC
(Using PWM is an unstable approximation)

## Slide 126: Kirchhoff's Current Law (KCL)
Gustav Kirchhoff
(1824-1887)
The sum of all currents entering a node equals the currents leaving the node
Conservation of Charge

## Slide 127: Kirchhoff's Voltage Law (KVL)
The sum of all voltages around a closed loop is zero
Conservation of Energy

## Slide 128: Series Resistor-Capacitor (RC) Circuit
KVL
Ohm's Law
KCL
Capacitive Current
R
C
VS

## Slide 129: Series Resistor-Capacitor (RC) Circuit
R
C
VS
The voltage across the charging capacitor as a function of time
KVL
Ohm's Law
KCL
Capacitive Current

## Slide 130: Unplug the MCU before changing any wiring!
As we move between each “experiment” on a given breadboard, or when we switch to an entirely new Board #, it is crucial that your FIRST UNPLUG the USB cord!
I recommend unplugging the cord at the PC end – leave the cord connected to the Micro USB port on the Pico
It is dangerous to change any wiring while the MCU is still drawing power from your laptop’s USB port
If you incorrectly connect a jumper wire between the Pico and the breadboard while the Pico is drawing power from your PC, you can permanently damage your PC’s USB port
Have your partner double-check your wiring every step!

## Slide 131: Wire Your Pico to Board 01
Black to GND
Yellow to (GP)IO22 pin
Blue to AD1 pin

## Slide 132: Wire Your Pico to Board 01

## Slide 133: Open rc_circuit.py





## Slide 134: View rc_circuit.py











## Slide 135: View rc_circuit.py










## Slide 136: View rc_circuit.py







## Slide 137: View rc_circuit.py





## Slide 138: Connect the Pico to Your PC
Plug the USB connector into your PC

## Slide 139: Run rc_circuit.py

## Slide 140: Run rc_circuit.py

## Slide 141: Check rc_circuit.py

## Slide 142


## Slide 143


## Slide 144: Check rc_circuit.py
Did your actual precisely match theory? Why not?

## Slide 145
The Value of Knowing How to Code

## Slide 146: Installing Software (Manually)

## Slide 147: Manually Update winget (only if necessary)
https://apps.microsoft.com/detail/9NBLGGH4NNS1
https://apps.microsoft.com/detail/9N0DX20HK701
https://github.com/PowerShell/PowerShell/releases

## Slide 148: Manually install VS Code (only if necessary)
https://code.visualstudio.com/download

## Slide 149: Manually install Git (only if necessary)
https://git-scm.com/install/windows

## Slide 150: Manually install Astral “uv” (only if necessary)
powershell -ExecutionPolicy ByPass -c "irm https://astral.sh/uv/install.ps1 | iex"
https://docs.astral.sh/uv/getting-started
Installing uv on Windows