## Slide 1
Dave Biersach
dbiersach@bnl.gov
Control System Electronics 101
Board 04
Signal Generators,
Operational Amplifiers,
RLC Resonance
Using Python and Sensors to Measure Circuits

## Slide 2: Board 04 – Goals – Part 1 of 2
Understand how a signal generator can create sine waves of oscillating voltage at a requested frequency
Learn about the Serial Peripheral Interface (SPI) and its strengths/weaknesses compared to the I2C interface
Create an oscilloscope by sampling and plotting captured waveform data
Analyze the negative feedback loop of an operational amplifier to understand how it achieves controllable gain

## Slide 3: Review Board 04
Board 04 will introduce you to a signal generator, an operational amplifier (Op Amp), and a resistor-capacitor-inductor (RLC) series circuit
100 nF Capacitor
22K Ω
Resistor
TLV2462
Op Amp
Signal
Generator
10K Ω
Resistor
10 Ω
Resistor
100 Ω
Resistor
100 mH Inductor

## Slide 4: Generating Sinusoids (Waves)
We want this:
We have this:
Solution:
Wire multiple RC circuits together each having different (time constants) to "add" waves together (superposition)

## Slide 5: AITRIP AD9833 – Signal Generator with SPI
https://www.amazon.com/gp/product/B09154XMGS

## Slide 6: Always Consult the Product Datasheet
https://www.analog.com/media/en/technical-documentation/data-sheets/ad9833.pdf
0 MHz to 12.5 MHz
Output Frequency Range
Trust nothing – measure everything 

## Slide 7: Analog Devices AD9833 Datasheet
Even though the range of a sine wave swings below zero, will we get a negative voltage?
Will the sine wave reach +3.3V at its maximum value?
Trust nothing – measure everything 

## Slide 8: Power Flow (Vcc = +3.3V)
Top
View
Bottom View
Analog Devices
AD988
Texas Instruments TLV2562
Vcc = Positive Collector (BJT)
same as
Vdd = Positive Drain (MOSFET)

## Slide 9: Power Flow (GND)
Texas Instruments TLV2562
Top
View
Bottom View
Analog Devices
AD988
SDATA
SCLK
FSYNC
= SPI Data
= SPI Clock
= SPI Chip Select

## Slide 10: Serial Peripheral Interface (SPI)
SCK = Serial Clock (to synchronize chips)
SDI = PICO = Peripheral In / Controller Out
SDO = POCI = Peripheral Out / Controller In
CS# = Chip Select ↔ FSYNC = Frame Sync

## Slide 11: Serial Peripheral Interface (SPI)
Controller (RP2040)
Peripheral(AD8933)

## Slide 12: SPI vs I2C
An SPI bus requires a dedicated (independent) Chip Select (CS) line per peripheral attached to the bus, which can quickly complicate wiring and increase manufacturing costs
But an I2C bus only needs two wires, which can be daisy-chained between components
Yes, the Adafruit Stemma-QT and SparkFun Qwiic cables add Vcc and GND wires to the standard I2C SDA and SCL wires, thus making four wires total - but this makes it easy to distribute power to all components with just one cable
However, at the signaling level, SPI is much faster than I2C. SPI is full-duplex at 50 MHz or higher, while I2C is message-based and has a typical bus speed of only 400 kHz

## Slide 13: Serial Peripheral Interface (SPI)

## Slide 14: Unplug the MCU before changing any wiring!
As we move between each “experiment” on a given breadboard or switch to an entirely new Board #, it is crucial that you FIRST UNPLUG the USB cord!
I recommend unplugging the cord at the PC end – leave the cord connected to the Micro USB port on the Pico
It is dangerous to change any wiring while the MCU is still drawing power from your laptop’s USB port. (NOTE: We will do this only during this Ohm’s Law lab on Board #3!)
If you incorrectly connect a jumper wire between the Pico and the breadboard while the Pico is drawing power from your PC, you can permanently damage your PC’s USB port
Have your partner double-check your wiring every step!

## Slide 15: Wire Your Pico to Board 04
YELLOW
RED
BLUE
BLACK
→ AD1
→ IO22
→ IO19
→ IO18
→ OUT
→ FSYNC
→ SDATA
→ SCLK

## Slide 16: Open signal_gen.py



## Slide 17: View signal_gen.py








## Slide 18: View signal_gen.py








## Slide 19: View signal_gen.py








## Slide 20: View signal_gen.py





## Slide 21: Connect the Pico to Your PC
If you incorrectly connect a jumper wire between the Pico and the breadboard, you can permanently damage your PC’s USB port!
Have your partner double-check your wiring before you plug in the USB cable back into your PC

## Slide 22: Run signal_gen.py
Recall our predictions for this experiment:
We should sample for 1 sec
We should see 30 peaks at 30 Hz
The max voltage should be ~0.68V
The voltage should not go below 0V

## Slide 24: The Value of Knowing How to Code
$4.25

## Slide 25: But what if we want to blink an LED?
A light emitting diode (LED) requires +2.0V to shine visible light, so we must figure a way to boost the output voltage of the AD9833 chip

## Slide 26: Operational Amplifiers
Here, we see a voltage divider placed on the Op-Amp output pin, with the middle tap routed back to the inverting input pin
An Op-Amp strives to keep a zero-voltage difference between the two input pins…
Output
Pin
Input Pins
Negative Feedback Loop
…when provided a negative feedback loop from the output
Rf = “Feedback” Resistor
OP AMP
This Op Amp circuit is a non-inverting amplifier that does not affect the phase of the input signal

## Slide 27: A Voltage Divider
KVL
Ohms
Ohms
KCL
+3.3V
330Ω
2KΩ
+ 2.83V
+ ?? V

## Slide 28: Operational Amplifiers
RF is the "feedback" resistor
RF and R2 form a voltage divider
Gain Formula for Op-Amp

## Slide 29: Operational Amplifiers
+3.3V
22K Ω
10K Ω
Max +0.68V
from the
AD9833
+2.18V 
TLV2462 Op Amp
This circuit generates a 3.2x gain
Non-Inverting Op-Amp Gain Formula

## Slide 30: Always Consult the Product Datasheet
https://www.ti.com/lit/gpn/tlv2462
+2.0V
20mA



rail
rail
Pin Out

Trust nothing – measure everything 

## Slide 31: Unplug the MCU before changing any wiring!
As we move between each “experiment” on a given breadboard or switch to an entirely new Board #, it is crucial that you FIRST UNPLUG the USB cord!
I recommend unplugging the cord at the PC end – leave the cord connected to the Micro USB port on the Pico
It is dangerous to change any wiring while the MCU is still drawing power from your laptop’s USB port. (NOTE: We will do this only during this Ohm’s Law lab on Board #3!)
If you incorrectly connect a jumper wire between the Pico and the breadboard while the Pico is drawing power from your PC, you can permanently damage your PC’s USB port
Have your partner double-check your wiring every step!

## Slide 32: Wire Your Pico to Board 04
Just move the yellow jumper down to the first tie point in Row 20
TLV2462
Op Amp

## Slide 33: Open op_amp.py



## Slide 34: View op_amp.py





## Slide 35: Connect the Pico to Your PC
If you incorrectly connect a jumper wire between the Pico and the breadboard, you can permanently damage your PC’s USB port!
Have your partner double-check your wiring before you plug in the USB cable back into your PC

## Slide 36: Run op_amp.py
Recall our predictions for this experiment:
The Op Amp provides a 3.2 gain
The max voltage is now ~2.18V
The Op Amp doesn’t affect phase

## Slide 37: This can blink a Red LED!

## Slide 38: Operational Amplifiers
Bill Hewlett
1913-2001
Wien Bridge Oscillator (1939)
Bill Hewlett & David Packard
HP 200A
https://en.wikipedia.org/wiki/Fantasound
(1940)
Bill Hewlett was 25 years old at the time

## Slide 39: The Mathematical Operations of an Op-Amp
"Adder"
"Subtractor"
"Differentiator"
"Integrator"

## Slide 40: An Operational Amplifier From Transistors
An Op Amp Implemented Using NPN BJTs
The Gain would be 3x
200k (RF)
100k (R2)

## Slide 41: Board 04 – Goals – Part 2 of 2
Understand how inductors store energy in a magnetic field
Differentiate impedance, resistance, and reactance
Appreciate that RLC circuits have a natural resonant frequency at which they oscillate
Simulate an RLC circuit using Euler's Method to numerically estimate its frequency response
Learn about how spectrum analyzers work and the value they provide engineers and technicians
Contrast the root mean squared (RMS) of a sinusoidal (alternating) signal versus using the simpler arithmetic mean to calculate the average value of the signal

## Slide 42: Inductors and Impedance
An inductor is a passive two-terminal electrical component that stores energy in a magnetic field when electric current flows through it. An inductor typically consists of an insulated wire wound into a coil
When the current flowing through the coil changes, the time-varying magnetic field induces a voltage which opposes the change in current that created it. As a result, inductors oppose any changes in current passing through them

## Slide 43: Inductors and Impedance
Inductors slow down current surges or spikes by temporarily storing energy in an electromagnetic field and then releasing it back into the circuit
Inductors are very common in power supplies, such as to create a buck or boost converter and they are common in radio circuits to create oscillators and filters
Electromagnets are the most often used inductors. Everything that moves due to electricity, such as relays, motors, solenoids, speakers, etc. uses inductors
Transformers are basically two inductors wound around the same core

## Slide 44: Inductors and Impedance

## Slide 45: Inductors and Impedance

## Slide 46: RLC Circuit – Total Impedance

## Slide 47: Inductors and Impedance

## Slide 48: An Undriven RLC Circuit
Lacking additional energy, the circuit's power drains away as it transforms into heat within the resistor.

## Slide 49: An Undriven RLC Circuit
Every RLC circuit has a specific fixed fundamental frequency in which it oscillates based on its
L and C values

## Slide 50: Driven Oscillators - Resonance
A system driven at its resonant frequency will experience maximum amplitude

## Slide 51: Driven Oscillators - Resonance
As the driving frequency pushes the circuit's oscillations closer to its resonant frequency, the circuit power will increase

## Slide 52: Driven Oscillators - Resonance
At the resonant frequency, the capacitive reactance in the LC components equals the inductive reactance, and therefore their impedance drops to zero – all that remains is the resistance of the R, L, C components
0

## Slide 53: Finding a Circuit’s Resonant Frequency
For simple circuits, like our RLC lab, we can directly compute the theoretical resonant frequency:
However, due to tolerance variations in the components, the actual resonant frequency might be reasonably away from its theoretical value
Circuits more complicated than a simple series RLC network might not even have a closed-form (analytic) formula expressing its resonant frequency, or the circuit might have multiple different regions of resonance

## Slide 54: A Driven RLC Circuit
TLV2462
Op Amp
VOUT
100nF
100mH
10Ω
100Ω
SPI Bus
The RLC Circuit is "powered" (driven) by the AD9833+TLV2462
We will measure the voltage at the 10Ω resistor

## Slide 55: Finding a Circuit’s Resonant Frequency

## Slide 56: Root Mean Squared (RMS) vs. Mean

What is the average power of this signal?

## Slide 57: Root Mean Squared (RMS) vs. Mean


But we are now only considering half of the full cycle!

## Slide 58: Root Mean Squared (RMS) vs. Mean
Mean is used to get the central tendency of a given data set while RMS is used when random variables given in the data are both negative and positive, such as in sinusoids




## Slide 59: Unplug the MCU before changing any wiring!
As we move between each “experiment” on a given breadboard or switch to an entirely new Board #, it is crucial that you FIRST UNPLUG the USB cord!
I recommend unplugging the cord at the PC end – leave the cord connected to the Micro USB port on the Pico
It is dangerous to change any wiring while the MCU is still drawing power from your laptop’s USB port. (NOTE: We will do this only during this Ohm’s Law lab on Board #3!)
If you incorrectly connect a jumper wire between the Pico and the breadboard while the Pico is drawing power from your PC, you can permanently damage your PC’s USB port
Have your partner double-check your wiring every step!

## Slide 60: Wire Your Pico to Board 04
Just move the yellow jumper up to Row 7

## Slide 61: Open rlc_measure.py

## Slide 62: View rlc_measure.py


## Slide 63: View rlc_measure.py









## Slide 64: View rlc_measure.py





## Slide 65: Connect the Pico to Your PC
If you incorrectly connect a jumper wire between the Pico and the breadboard, you can permanently damage your PC’s USB port!
Have your partner double-check your wiring before you plug in the USB cable back into your PC

## Slide 66: Run rlc_measure.py

## Slide 67: Open rlc_plot_actual.py



## Slide 68: View rlc_plot_actual.py







## Slide 69: Run rlc_plot_actual.py

## Slide 70: Simulating a Driven RLC Circuit
Charge (in Coulombs)
Current (in Amps)
S
R
L
C
AC Voltage Source
Ohm's Law
Faraday's Law
Gauss's Law
Kirchhoff's Voltage Law
10.20Ω 99.50Ω
101.6mH
93.7
uF
Euler's Method
Voltage across the resistor

## Slide 71: Open rlc_plot_theory.py







## Slide 72: View rlc_plot_theory.py




## Slide 73: View rlc_plot_theory.py

## Slide 74: Run rlc_plot_theory.py

## Slide 75: Check rlc_plot_theory.py
At resonance, the LC elements have nearly zero resistance, so the current (and hence voltage) flowing through R1 (and R2) would be at the maximum

## Slide 76: Check rlc_plot_theory.py
Engineers must contend with the real world where nothing is exact or consistent

## Slide 77: Finding a Circuit’s Resonant Frequency
A spectrum analyzer (SA) is an advanced benchtop instrument used to measure a circuit's response as the circuit's inputs are systematically swept across a wide range of frequencies
By plotting circuit measurements like output voltage, the SA can help identify the frequencies that induce resonance
This analysis is crucial when designing radios and antennas that can transmit and receive signals at specific frequencies
We need a SA to design and test cell towers, Wi-Fi stations, GPS satellites, radar detectors, laser ranging devices, and even acoustical instruments

## Slide 78: The Value of Knowing How to Code
