## Slide 1
Dave Biersach
dbiersach@bnl.gov
Control System Electronics 101
Board 05
Decibels,
Twin-T Notch Filter, Harmonics
Using Python and Sensors to Measure Circuits

## Slide 2: Board 05 – Goals
Define the concept of a decibel, and identify why it is a useful measure in signal analysis
Calculate the relationship between -3dB and the halving of a signal’s power/intensity
Examine the range of human hearing in terms of Hertz
Consider the difference between a sine wave and a square wave in terms of higher-order harmonics
Review simple passive RC filters (low pass and high pass)
Construct a Twin-T Notch filter circuit and evaluate its band-stop capabilities

## Slide 3: A Decibel (1/10th of a Bel)
Origin: The decibel (dB) was developed at Bell Telephone Laboratories in the 1920s to quantify signal loss over telephone lines. It is named after Alexander Graham Bell
Logarithmic ratio: A decibel expresses the ratio between two power levels as 10·log₁₀(P₂/P₁), compressing huge dynamic ranges into manageable numbers
Human perception: Our ears perceive loudness logarithmically — a 10 dB increase sounds roughly twice as loud — making dB a natural fit for audio work
Reference standards: Absolute measurements require a reference scale/unit; common ones include dBm (1 mW) and dBV (1 volt)

## Slide 4: Decibels
Additive convenience: Because logs turn multiplication into addition, cascaded gains and losses simply add: a 20 dB amp feeding a 6 dB cable loss yields +14 dB overall
Universal adoption: Decibels appear across electronics, acoustics, RF engineering, and signal processing wherever signals span many orders of magnitude
Some examples:
  An amplifier with 1 W input and 100 W output: 10·log₁₀(100/1) = +20 dB gain
  A cable losing half the signal power: −3 dB
  Feeding 50 mW into a system referenced to 1 mW: 10·log₁₀(50/1) ≈ +17 dBm
  A voltage divider cutting voltage to 1/10: 20·log₁₀(0.1) = −20 dB

## Slide 5: Decibels

## Slide 6: Decibels




## Slide 7: Decibels

## Slide 8: Why 3dB ??

## Slide 9: Decibels

## Slide 10: The Range of Human Hearing



## Slide 12: Sine vs. Square Waves
In the first part of this lab, we will use the AD9833 Signal Generator on Board 04 to generate a 750 Hz frequency tone
That frequency is well within the comfortable hearing range of humans – we will attach a speaker to listen to the tone
We will generate both a pure sine wave at 750 Hz, and then a square wave also at 750Hz
Recall from Topic 01 Fourier Analysis, that a square wave is composed of a series of cosine waves: it is a superposition of an infinite number of odd harmonics that have decreasing amplitudes

## Slide 13
Cosine is an EVEN function -
symmetric around its midpoint
Sine is an ODD function -antisymmetric around its midpoint
Discontinuous jumps can be approximated only by an infinite sum of sinusoids

## Slide 14: Square Wave – Odd Harmonics Only

## Slide 15: Unplug the MCU before changing any wiring!
As we move between each “experiment” on a given breadboard or switch to an entirely new Board #, it is crucial that you FIRST UNPLUG the USB cord!
I recommend unplugging the cord at the PC end – leave the cord connected to the Micro USB port on the Pico
It is dangerous to change any wiring while the MCU is still drawing power from your laptop’s USB port
If you incorrectly connect a jumper wire between the Pico and the breadboard while the Pico is drawing power from your PC, you can permanently damage your PC’s USB port
Have your partner double-check your wiring every step!

## Slide 16: Wire Your Pico to Boards 04 and 05
Board 04
Board 05
(3) BLACK Jumpers
(3) RED Jumpers
BLUE Jumper
(1) YELLOW Jumper

## Slide 17: Open notch_filter.py




## Slide 18: View notch_filter.py







## Slide 19: Connect the Pico to Your PC
If you incorrectly connect a jumper wire between the Pico and the breadboard, you can permanently damage your PC’s USB port!
Have your partner double-check your wiring before you plug in the USB cable back into your PC

## Slide 20: Run notch_filter.py
You should hear the tones in the breadboard speaker
https://www.adafruit.com/product/1898 - $1.85
However, the timbre (tonal quality or color of a sound) of the sine versus the square wave is clearly different, even though they are the exact same frequency (750 Hz)
The odd higher harmonics in the square wave make it sound buzzy
The pure sine wave has only the fundamental harmonic

## Slide 21: Filter Types
We can design circuits to filter signals.
We can allow or block
ranges of frequencies within a given signal.

## Slide 22: A Passive Low Pass Filter
At low frequencies, the capacitor looks like an open circuit and doesn’t interfere with the signal
At high frequencies, the capacitor allows current to easily flow to ground, creating a short circuit and shunting the output

## Slide 23: A Passive Low Pass Filter

## Slide 24: A Passive High Pass Filter
At low frequencies, the capacitor looks like an open circuit and blocks the signal
At high frequencies, the capacitor allows current to easily flow through it, and doesn’t interfere with the signal

## Slide 25: A Passive High Pass Filter

## Slide 26: Modelling Low and High Pass Filters
Using software, we can calculate the response of a low-pass and a high-pass filter over a range of input frequencies
If both filters have similar resistors and capacitors, then they will have the same cutoff frequency:
At this special “cutoff” frequency, due to the loading effects of the resistor and capacitor, the signal will have lost 50% of its power, so it is referred to as the -3 dB point
Cutoff really means the point “where attenuation starts to matter” rather than “signal stops here.”

## Slide 27: Modelling Low and High Pass Filters
V_cap
V_R
We can estimate the voltage drop across the capacitor (V_cap) and resistor (V_R) at signal frequencies of 0 Hz, 1592 Hz, and 100 kHz

## Slide 28: Open rc_filter.py





## Slide 29: View rc_filter.py




## Slide 30: View rc_filter.py

It's named after Hendrik Wade Bode (1905–1982), an American engineer who worked at Bell Labs.

## Slide 31: View rc_filter.py






## Slide 32: View rc_filter.py



AD9833 doesn’t emit negative volts



## Slide 33: View rc_filter.py





## Slide 34: View rc_filter.py



## Slide 35: Run rc_filter.py

## Slide 36: Check rc_filter.py

In LP filter – no drop across cap (open circuit) so V_cap matches input Vs
In HP filter – no current thru cap, so no voltage into R
In LP filter – cap is half shunted, so now V_cap is lower than Vs
In HP filter – cap is starting to pass current, so V_R rises
In LP filter – Cap now full shunts to GND so no V_cap
In HP filter – Full Vs makes it to the R, and the capacitor is “blocking” DC



## Slide 37: Testing LP and HP Filters on an Oscilloscope

## Slide 38: Testing LP and HP Filters on an Oscilloscope

## Slide 39: Testing LP and HP Filters on an Oscilloscope

## Slide 40: Combining a Low Pass and High Pass Filter
Combining a low-pass and high-pass filter allows you to isolate a specific range of frequencies, passing only those between the two cutoff points while attenuating everything above and below in frequency
By arranging the filters in parallel rather than series, signals can pass around a specific frequency range: the low-pass handles frequencies below the notch while the high-pass handles frequencies above, creating a rejection band in the middle
The Twin-T notch filter was developed by Herbert E. Kallmann in 1940 while working on television circuits; it could achieve a sharp notch using only passive components without inductors, which were bulky and expensive

## Slide 41: A Twin-T Notch Filter

## Slide 42: Resistors and Capacitors in Parallel
R / 2
2C

## Slide 43: Board 05 Twin-T Filter
Capacitors in Parallel = 2C
Resistors in Parallel = R/2
Op Amp (3.2x Gain)

## Slide 44: Combining a Low Pass and a High Pass Filter

## Slide 45: Notching Out the Fundamental Freq
Our Twin-T filter notches out (-35 dB gain) the frequencies around 740-760 Hz
If we generate a pure sine wave at 750 Hz, we should not hear it pass through the Twin-T filter
But the higher-order odd harmonics of a square wave should pass through the filter
The Op Amp is there to amplify those higher harmonics of the square wave fundamental frequency, because their amplitudes fall off very quickly

## Slide 46: Square Wave – Odd Harmonics Only

## Slide 47: Unplug the MCU before changing any wiring!
As we move between each “experiment” on a given breadboard or switch to an entirely new Board #, it is crucial that you FIRST UNPLUG the USB cord!
I recommend unplugging the cord at the PC end – leave the cord connected to the Micro USB port on the Pico
It is dangerous to change any wiring while the MCU is still drawing power from your laptop’s USB port
If you incorrectly connect a jumper wire between the Pico and the breadboard while the Pico is drawing power from your PC, you can permanently damage your PC’s USB port
Have your partner double-check your wiring every step!

## Slide 48: Wire Your Pico to Boards 04 and 05
Board 04
Board 05
Simply move the yellow jumper from Board 04 down to the tie point 21 on Board 05

## Slide 49: Run notch_filter.py
Which wave type (tone) passes through the filter?
This would happen even if we just used a GPIO pin to manually create a square wave by alternatively raising and lowering the pin’s voltage (think how we manually blinked the RED LED on Board 01)
It is inescapable that the mere act of trying to make a square wave will generate sinusoidal higher odd harmonic waves
Mother Nature abhors square waves – they are not naturally occurring in any phenomenon
You are listening to a live demonstration of the Fourier Transform!